## Slide 1
🌤️ VayuSurya AI
AI-Based Renewable Energy Generation Forecasting
Theme 10
KREDL / KSPDCL
Karnataka
Team VSA — Kuldeep Parmar · Nishchal Soni · Ankit Mewada · Piyush Saini
"Like a weather-wise plant operator who never sleeps"
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 2
⚡ The Problem
🌦️
Weather Variability
Solar output depends on cloud cover & irradiation. Wind varies with speed & direction. Generation is inherently unpredictable.
⚙️
System Constraints
Existing SCADA/EMS systems cannot be modified. Solution must work as an overlay layer — no replacements allowed.
📊
Forecasting Gaps
Day-ahead, intra-day & hourly forecasts needed. Uncertainty must be quantified. Explanations required for operators.
⚠️ Impact: Scheduling inefficiencies → Curtailment losses → Grid imbalance → Backup (thermal) over-reliance
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 3
💡 Our Solution
VayuSurya AI is a forecasting layer that learns how each solar plant and wind cluster behaves under changing weather — and tells planners what's coming, with confidence.
📅 Day-Ahead Forecast
24-hour predictions for operational planning
🔄 Intra-Day Updates
6-hour rolling updates as weather changes
⏱️ Hourly Predictions
Granular hour-by-hour generation estimates
📊 Uncertainty Bands
P10 / P50 / P90 confidence intervals always included
🔍 SHAP Explainability
Shows exactly which weather driver caused each change
🔒 No System Changes
Read-only overlay — zero modification to existing systems
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 4
🏗️ How It Works
🌤️
Weather Data
+ Historical Gen
▶
⚙️
Feature
Engineering
▶
🤖
QRF Model
(50 trees)
▶
📊
P10/P50/P90
Output
▶
💡
SHAP
Explainability
Feature Engineering
▸ irr_cloud_interaction = Irradiance × (1 − cloud/100)
▸ wind_cube = ((ws−3)/9)² [power curve]
▸ temp_derating = 1 − 0.004 × max(0, T−25)
▸ hour_sin / hour_cos [cyclic time encoding]
▸ wind_dir_cos [direction-aware component]
Quantile Regression Forest
▸ 50 decision trees in ensemble
▸ Bootstrap sampling per tree
▸ P10 = 10th percentile of all tree outputs
▸ P50 = median forecast (best estimate)
▸ P90 = 90th percentile (upper bound)
▸ No external ML library needed
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 5
📊 Uncertainty & Explainability
Uncertainty Quantification
Hour →
▸ P10 = Lower bound (pessimistic)
▸ P50 = Point forecast (best estimate)
▸ P90 = Upper bound (optimistic)
▸ Band width = forecast uncertainty
▸ Color coded: Green / Amber / Red
▸ Alert triggered when uncertainty > 20%
SHAP Explainability
☀️ Irradiance
38%
☁️ Cloud Cover
28%
💨 Wind Speed
20%
🌡️ Temperature
8%
🕐 Time of Day
6%
→ Operators see WHY generation changed, not just what was predicted
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 6
🗺️ Karnataka Coverage
☀️
Bellary Solar Cluster
Solar
250 MW
installed capacity
💨
Chitradurga Wind Farm
Wind
180 MW
installed capacity
☀️
Tumkur Solar Park
Solar
200 MW
installed capacity
💨
Davangere Wind Cluster
Wind
150 MW
installed capacity
☀️
Hassan Solar Plant
Solar
120 MW
installed capacity
💨
Bidar Wind Cluster
Wind
100 MW
installed capacity
Total Coverage: 6 regions | 3 Solar + 3 Wind | 1,000 MW total capacity | Single unified model for all
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 7
✅ Non-Negotiables — 100% Compliant
✓
Existing systems not modified or replaced
Pure read-only forecasting layer — zero changes to SCADA/EMS
✓
Works as forecasting overlay layer
Consumes data copies only; no writes to any operational system
✓
Works with masked / synthetic data
Built entirely on Karnataka synthetic data — no real data required
✓
Forecasts must be explainable
SHAP-style permutation importance shows driver for every prediction
✓
Uncertainty explicitly represented
P10/P50/P90 bands + per-hour uncertainty chart on dashboard
✓
No hosted LLM on sensitive data
Pure ML model (QRF) — zero LLM usage anywhere in the system
✓
Generalizes across assets & geographies
Single architecture works for solar + wind across all 6 regions
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 8
🔒 Privacy & Data Handling
🔒 On-Prem Deployment
▸ Runs inside KREDL's secure environment
▸ No data leaves Karnataka
▸ No cloud dependency required
🎭 Synthetic Data
▸ Real generation data masked for demo
▸ Synthetic profiles match Karnataka regions
▸ Fully privacy compliant
🚫 No LLM Usage
▸ Zero hosted LLM anywhere in pipeline
▸ Pure statistical ML model only
▸ No sensitive data sent externally
📋 Data Pipeline
▸ AI layer reads data copies only
▸ No writes to existing systems
▸ Missing values → rolling average imputation
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 9
🔮 Roadmap & Impact
Phase 1 · Current
Working Prototype
✓ Synthetic data pipeline
✓ QRF model (solar+wind)
✓ Streamlit dashboard
✓ SHAP explainability
Phase 2 · Month 1
Integration
✓ Real IMD weather API
✓ REST API endpoint
✓ Masked data ingestion
✓ Intra-day automation
Phase 3 · Month 2-3
Production
✓ LSTM/XGBoost hybrid
✓ Auto-retraining pipeline
✓ Drift detection alerts
✓ 99.5% SLA deployment
Expected Impact
~20-38%
RMSE improvement
over baseline
~80%
Confidence band
coverage
24/7
Continuous
forecasting
0
System
modifications
VayuSurya AI | AI for Bharat — Theme 10 | KREDL / KSPDCL

## Slide 10
⚡ VayuSurya AI
Powering Karnataka's Renewable Future
✅ Accurate P10/P50/P90 forecasts for solar & wind across Karnataka
✅ Explicit uncertainty quantification — no more guesswork
✅ SHAP explainability — operators know WHY, not just what
✅ Zero system modifications — pure read-only overlay
✅ Works with synthetic/masked data — privacy compliant
✅ Single model generalizes across all assets & geographies
🔗 github.com/kuldeep811p/VayuSurya-AI | Team VSA | AI for Bharat — Theme 10